## Slide 1: GPU-based Global Drone Localization
Jizhou Yan

## Slide 2: Agenda
Overview
Data Collection
Proof of Concept
Further Work

## Slide 3: Overview
Localization is required for auto-navigation
Typical vision-based localization method:
Feature detection
feature matching
Estimate Camera Pose
Capture Image Frame

## Slide 4: Data Collection
GRASP Lab
Scene Data: 500+ images, build with Structure-from-Motion
Test Data: 100 images
Ground truth: motion capture system

## Slide 5: Data Collection
Scene Data Test Data

## Slide 6: Data Collection
3D feature point cloud

## Slide 7: Proof of Concept
On-board work flow
  Extract SIFT feature
  Feature matching
  linear method to estimate camera pose (PnP)
  Non-linear method to estimate camera pose
Using OpenCV SIFT (cpu) & KD-Tree
Own implement of PnP and non-linear optimization

## Slide 8: Proof of Concept
Compare with mo-cap data

## Slide 9: Proof of Concept
Compare with mo-cap data
Error: 11.51mm

## Slide 10: Further Work
Implement and evaluate SIFT feature extraction