## Slide 1: GPU-based Global Drone Localization
Jizhou Yan

## Slide 2: Outline
Implementation
Find best parameter
Plan

## Slide 3: Implementation
Test platform
  Tegra K1 SOC
  NVIDIA Kepler GPU with 192 CUDA Cores
  Quad-Core ARM® Cortex™-A15 CPU
  2GB Memory
Performance
  SIFT FPS: 21.7
  Localization FPS: 16.1
  RMSE: 17.4 mm

## Slide 4: Implementation
Result on test dataset

## Slide 5: Implementation
Number of feature: 100
Number of Octave layers: 3
Contrast threshold: 0.1
Edge Threshold: 20
Sigma: 1.6
Sub-pixel interpolation: yes

## Slide 6: Find best parameter
Number of feature
Number of Octave layers
Contrast threshold
Edge Threshold
Sigma
Sub-pixel interpolation

## Slide 7: Find best parameter
Number of feature: 100
Chart: Number of Feature
| 20 | 100 | 200 | 500 | 1000
FPS | 33.2 | 21.7 | 17.3 | 15.1 | 13.5
RMSE | 95.6 | 17.4 | 13.6 | 12.2 | 11.4

## Slide 8: Find best parameter
Number of Octave layers: 3
Chart: Number of Octave layers
| 1 | 3 | 5 | 7
FPS | 24.2 | 21.7 | 18.3 | 15.1
RMSE | 34.2 | 17.4 | 16.6 | 17.2

## Slide 9: Find best parameter
Contrast threshold: 0.1
Edge Threshold: 20

## Slide 10: Plan
Current FPS is not enough
Implement parallel optical-flow
SIFT Extraction
Matching
Camera Pose Estimation
Optical-Flow Tracking
New Frame